## Slide 1: More about Loop Optimization
Cong (Callie) Hao
callie.hao@ece.gatech.edu
Assistant Professor
ECE, Georgia Institute of Technology
  Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/

## Slide 2: Hardware Design with HLS
Where does performance gain come from?
Specialization
Parallelization
Data-type
  Arbitrary fixed-point precision, customized floating-point precision
Memory and data movement
  Customized data storage in banks
  Customized data loading and feeding
Computation
  How do you schedule the computations?
    Order, granularity, etc.
Operation level parallelism
  Multiple operations or instructions executed simultaneously
  Mostly about loop manipulation and data partitioning
Task level parallelism (TLP)
  Dataflow and streaming
  Overlapped compute and data movement

## Slide 3: Put-together: Pipeline + Unroll +Partition
The three techniques are frequently used together to boost computation efficiency
#pragma HLS array_partition variable=A dim=2 complete
#pragma HLS array_partition variable=B dim=2 complete
#pragma HLS array_partition variable=C dim=2 complete
for (int i = 0; i < N; i++) {
#pragma HLS pipeline II=1
for (int j = 0; j < M; j++) {
#pragma HLS unroll
A[i][j] = B[i][j] * C[i][j];
}
}
i=0
i=1
i=2
i=0
i=1
i=2
Outer loop pipelining will enforce all inner loops fully unrolled. Why?

## Slide 4: HLS Pragmas
A lot of useful “pragma”s: tell your compiler how to build the hardware
This link has all the pragmas you need:
  https://docs.xilinx.com/r/en-US/ug1399-vitis-hls/HLS-Pragmas

## Slide 5: More HLS Resources
This link has everything you need to know about HLS…
  https://docs.xilinx.com/r/en-US/ug1399-vitis-hls/Getting-Started-with-Vitis-HLS
  I can be 100% substituted by this link 
  … or can I ???
Remember: using HLS for FPGA design is NOT all about playing with pragmas
It’s you designing an architecture, using HLS to achieve your goal
Let me see what are those pragmas?
Try to use them to optimize my design
I want to optimize my design in such a way… (e.g., hey, these operations can be parallelized!)
Let me check if there’s a pragma (with code rewrite) that can achieve my goal

## Slide 6: Put-together: Pipeline + Unroll +Partition
The three techniques are frequently used together to boost computation efficiency
#pragma HLS array_partition variable=A dim=2 complete
#pragma HLS array_partition variable=B dim=2 complete
#pragma HLS array_partition variable=C dim=2 complete
for (int i = 0; i < N; i++) {
#pragma HLS pipeline II=1
for (int j = 0; j < M; j++) {
#pragma HLS unroll
A[i][j] = B[i][j] * C[i][j];
}
}
i=0
i=1
i=2
i=0
i=1
i=2

## Slide 7: Effective Region of Unroll and Pipeline
void top( ports ) {
for(int i = 0; i < 512; i++) {
for(int j = 0; j < 1024; j++) {
#pragma HLS pipeline
sum[i] += A[i][j] * B[i][j];
}
}
}
Both Pipeline and Unroll must act on a loop, i.e., within a loop region
j
j
i=0
i=1

## Slide 8: Effective Region of Unroll and Pipeline
void top( ports ) {
for(int i = 0; i < 512; i++) {
for(int j = 0; j < 1024; j++) {
#pragma HLS unroll
sum[i] += A[i][j] * B[i][j];
}
}
}
Both Pipeline and Unroll must act on a loop, i.e., within a loop region
j
i=0
j
i=1

## Slide 9: Effective Region of Unroll and Pipeline
void top( ports ) {
for(int i = 0; i < 512; i++) {
#pragma HLS pipeline
for(int j = 0; j < 1024; j++) {
#pragma HLS unroll
sum[i] += A[i][j] * B[i][j];
}
}
}
Both Pipeline and Unroll must act on a loop, i.e., within a loop region
j
i=0
j
i=1
j
i=2
Note: the pipeline will enforce the inner loop being completely unrolled!
Could cause great scalability issue – discuss later

## Slide 10: Effective Region of Unroll and Pipeline
void top( ports ) {
for(int i = 0; i < 512; i++) {
#pragma HLS pipeline
#pragma HLS unroll
for(int j = 0; j < 1024; j++) {
sum[i] += A[i][j] * B[i][j];
}
}
}
Putting both pipeline and unroll together? WRONG! Pick only one!
The inner loops are untouched
Outer loop is unrolled: generate 512 copies of i loop body
The inner loops (j) are all unrolled
And the unrolled statements will be pipelined

## Slide 11: Unroll v.s. Pipeline
When to use which?
 | Pipeline | Unroll
Impact on inner loops | Enforce to be unrolled | No
Impact on inner functions | Enforce to be inlined | No
Loop-carried dependency | Handles dependency by staging | Cannot parallelize if there’s dependency
Resource usage | Reuse resource across iterations | Replicates resources for each unrolled copy
Nested loops | Used in outer loops | Used in inner loops

## Slide 12: More Loop Optimizations
Initial Interval (II) Violation
Loop-carried Dependency
  Loop reorder
  Remove false dependency
Pipeline and Unroll over Functions
Loop Tiling and Partial Unroll
Loop Fusion
  Parallel loops fused into single loop
  Wrap loops into functions

## Slide 13: A very Common Error: II Violation
What does II > 1 mean?
Pipeline is ready, but something blocks it from starting every cycle
Two Root Causes (99% of cases)
1️⃣ Resource Limitation: hardware cannot support one iteration per cycle
Common symptoms: Memory port limitation, Array not partitioned, Too many operations scheduled in one cycle, DRAM (m_axi) accessed inside a pipeline
Typical fixes: Partition on-chip arrays (array_partition), Copy data from DRAM to local buffers (BRAM / registers), Reduce unroll factor, Use loop tiling to control parallelism
2️⃣ Loop-Carried Dependency: An iteration depends on results from previous iterations.
Common symptoms: Accumulation (sum += ...), Read-after-write on the same variable, Conservative dependency assumed by HLS
Typical fixes: Reorder loops, Use local buffers or shift registers, Build an adder tree (avoid in-loop accumulation), Remove false dependency only if proven safe, (#pragma HLS dependence inter false)

## Slide 14: The most important factor about pipelining
Initial Interval (II) – II violation
i=0
i=1
i=2
II = 1
II = 2
i=0
i=1
i=2

## Slide 15: Causes to II violation
Not enough resource (e.g., memory not partitioned)
void test(int sum[10], int A[10][100], int B[10][100])
{
for(int i = 0; i < 10; i++) {
#pragma HLS pipeline
for(int j = 0; j < 100; j++) {
sum[i] += A[i][j] * B[i][j];
}
}
}

## Slide 16: Causes to II violation
Not enough resource (e.g., memory not partitioned)
void test(int sum[10], int A[10][100], int B[10][100])
{
for(int i = 0; i < 10; i++) {
#pragma HLS pipeline
for(int j = 0; j < 100; j++) {
sum[i] += A[i][j] * B[i][j];
}
}
}
WARNING: [HLS 200-885] Unable to schedule 'load' operation ('A_load_2', top.cpp:63) on array 'A' due to limited memory ports. Please consider using a memory core with more ports or partitioning the array 'A'.
Resolution: For help on HLS 200-885 see …
INFO: [HLS 200-1470] Pipelining result : Target II = 1, Final II = 50, Depth = 52, …

## Slide 17: Causes to II violation
Manual array partition
void test(int sum[10], int A[10][100], int B[10][100])
{
#pragma HLS array_partition variable=A dim=2 complete
#pragma HLS array_partition variable=B dim=2 complete
for(int i = 0; i < 10; i++) {
#pragma HLS pipeline
for(int j = 0; j < 100; j++) {
sum[i] += A[i][j] * B[i][j];
}
}
}

## Slide 18: Causes to II violation
[Caution!] If array is from DRAM – copy to local buffer (BRAM) first!
void test(int sum[10], int A[10][100], int B[10][100])
{
#pragma HLS interface m_axi port=A offset=slave bundle=mem
#pragma HLS interface m_axi port=B offset=slave bundle=mem
#pragma HLS interface m_axi port=sum offset=slave bundle=mem
#pragma HLS array_partition variable=A dim=2 complete
#pragma HLS array_partition variable=B dim=2 complete
// copy A to A_local, B to B_local
for(int i = 0; i < 10; i++) {
#pragma HLS pipeline
for(int j = 0; j < 100; j++) {
sum_local[i] += A_local[i][j] * B_local[i][j];
}}}
A, B, and sum are from DRAM; cannot partition DRAM!

## Slide 19: More Loop Optimizations
Initial Interval (II) Violation
Loop-carried Dependency
  Loop reorder
  Remove false dependency
Pipeline and Unroll over Functions
Loop Tiling and Partial Unroll
Loop Fusion
  Parallel loops fused into single loop
  Wrap loops into functions

## Slide 20: Loop-carried Dependency
An iteration of a loop depends on a result produced by a previous iteration, which takes multiple cycles to complete
Can be true or false dependency
  HLS tends to be conservative
Write to Mem[i+1]
Read from Mem[i+1]
Write to Mem[i+2]
Initial Interval (II) = 6

## Slide 21: If True Dependency?
void test(float w, float mem[100])
{
for(int i = 1; i < 100; i++) {
#pragma HLS pipeline
float a = mem[i-1];
mem[i] = a * w;
}
}
Initial Interval (II) = 5
Mem[0]
Read
Mem[1]
Write
FP mul
Mem[1]
Read
Mem[2]
Write
FP mul

## Slide 22: If True Dependency with Another Dimension
#pragma HLS array_partition variable=mem dim=1 complete
void test(float w, float mem[10][100])
{
for(int j = 0; j < 10; j++) {
#pragma HLS unroll
for(int i = 1; i < 100; i++) {
float a = mem[j][i-1];
mem[j][i] = a * w;
}
}
}
…

## Slide 23: If False Dependency? Remove it!
But only do it when you’re sure it’s safe
void test(int* A, float B[100])
{
for(int i = 0; i < 100; i++) {
int x = A[i];
B[x] *= B[x];
}
}
B[x] read
B[x] write
B[x] read
…
Don’t know if they’re the same B[x]
So II = 3

## Slide 24: If False Dependency? Remove it!
But only do it when you’re sure it’s safe
void test(int* A, float B[100])
{
#pragma HLS DEPENDENCE variable=B inter false
for(int i = 0; i < 100; i++) {
int x = A[i];
B[x] *= B[x];
}
}
But if you know for sure: e.g., array A is monotonically increasing
II = 1

## Slide 25: Summary for now
Critical Warnings
Outer loop pipelining forces inner loop full unrolling → Can easily cause resource explosion
Floating-point accumulation almost always causes II > 1 → FP adder latency > 1 cycle
DRAM arrays cannot be partitioned → Always copy to local memory before pipelining/unroll
Dependence inter false is a promise, not a hint → If you are wrong, the bug is yours
Debugging Checklist
  Check achieved II in the HLS report
  If II > 1 → identify resource vs dependency
  Fix memory first, then dependency
  Control parallelism before increasing it

## Slide 26: More Loop Optimizations
Initial Interval (II) Violation
Loop-carried Dependency
  Loop reorder
  Remove false dependency
Pipeline and Unroll over Functions
Loop Tiling
Loop Fusion
  Parallel loops fused into single loop
  Wrap loops into functions

## Slide 27: Pipeline and Unroll over Functions
Pipeline over function: the function must be inlined
Unroll over function: the function will be duplicated

## Slide 28: Pipeline over Function
If a function inside pipeline region – the function must be inlined
void test(int sum[10], int A[10][100], int B[10][100])
{
#pragma HLS array_partition variable=A dim=1 complete
#pragma HLS array_partition variable=B dim=1 complete
for(int i = 0; i < 10; i++) {
#pragma HLS pipeline II=1
sum[i] += foo(A[i], B[i]);
}
}
int foo(int A[100], int B[100])
{
#pragma HLS inline
int add = 0;
for(int i = 0; i < 10; i++)
add += A[i] * B[i];
return add;
}

## Slide 29: Unroll over Function
Unroll a loop involving a function – the function will be duplicated
void test(int sum[10], int A[10][100], int B[10][100])
{
#pragma HLS array_partition variable=A dim=1 complete
#pragma HLS array_partition variable=B dim=1 complete
#pragma HLS array_partition variable=sum complete
loop_L1: for(int i = 0; i < 10; i++) {
#pragma HLS unroll
sum[i] = foo(A[i], B[i]);
}
}
int foo(int A[100], int B[100])
{
int add = 0;
for(int i = 0; i < 10; i++)
add += A[i] * B[i];
return add;
}
foo is duplicated by 10 copies which run in parallel

## Slide 30: More Loop Optimizations
Initial Interval (II) Violation
Pipeline and Unroll over Functions
Loop-carried Dependency
  Loop reorder
  Remove false dependency
Loop Tiling and Partial Unroll
Loop Fusion
  Parallel loops fused into single loop
  Wrap loops into functions

## Slide 31: Loop Tiling – Controlled Parallelism
When you have multiple loops, or the loop count is too big
void test(int A[1024][1024], int B[1024][1024], int sum[1024])
{
// array_partition omitted for(int i = 0; i < 1024; i++) {
#pragma HLS pipeline
for(int j = 0; j < 1024; j++) {
sum[i] += A[i][j] * B[i][j];
}
}
}
Unable to pipeline, crashes, or hangs forever

## Slide 32: Loop Tiling – Controlled Parallelism
Step 1: break them into tiles
Step 2: parallelize within one tile
Step 3: pipeline across different tiles
  We’ll see another example of II violation

## Slide 33: Step 1: Break into Tiles
void test(int A[1024][1024], int B[1024][1024], int sum[1024])
{
L1: for(int i = 0; i < 1024; i++) { L2: for(int j = 0; j < 1024; j += 16) {
L3: for(int jj = 0; jj < 16; jj++) {
sum[i] += A[i][j + jj] * B[i][j + jj];
}}}}
Let these 16 multiplications execute in parallel

## Slide 34: Step 2: Parallelize with one tile
void test(int A[1024][1024], int B[1024][1024], int sum[1024])
{
#pragma HLS array_partition variable=A dim=2 factor=16 cyclic
#pragma HLS array_partition variable=B dim=2 factor=16 cyclic
L1: for(int i = 0; i < 1024; i++) { L2: for(int j = 0; j < 1024; j += 16) {
L3: for(int jj = 0; jj < 16; jj++) {
#pragma HLS unroll
sum[i] += A[i][j + jj] * B[i][j + jj];
}}}}

## Slide 35: Step 3: Pipeline across Different Tiles
void test(int A[1024][1024], int B[1024][1024], int sum[1024])
{
#pragma HLS array_partition variable=A dim=2 factor=16 cyclic
#pragma HLS array_partition variable=B dim=2 factor=16 cyclic
L1: for(int i = 0; i < 1024; i++) { L2: for(int j = 0; j < 1024; j += 16) {
#pragma HLS pipeline L3: for(int jj = 0; jj < 16; jj++) {
#pragma HLS unroll
sum[i] += A[i][j + jj] * B[i][j + jj];
}}}}

## Slide 36: [Caution!] You May Run into II Violation
Not because of multiplication but because of the accumulation
* | * | * | * | * | * | * | *
Sum[i]
16 multiplications can be done in 1 cycle but not the fixed_point or floating_point accumulation…

## Slide 37: This is the II Violation in Vitis HLS Scheduler

## Slide 38: Resolve the II Violation
void test(FIX_TYPE A[1024][1024], FIX_TYPE B[1024][1024], FIX_TYPE sum[1024])
{
#pragma HLS array_partition variable=A dim=2 factor=16 cyclic
#pragma HLS array_partition variable=B dim=2 factor=16 cyclic
L1: for(int i = 0; i < 1024; i++) { L2: for(int j = 0; j < 1024; j += 16) {
#pragma HLS pipeline
FIX_TYPE sum_local[16]; L3: for(int jj = 0; jj < 16; jj++)
sum_local[jj] = A[i][j + jj] * B[i][j + jj];
L4: for(int k = 0; k < 16; k++)
sum[i] += sum_local[k];
}}}
L3: for(int jj = 0; jj < 16; jj++)
sum[i] += A[i][j + jj] * B[i][j + jj];
Use a partitioned local buffer (registers)

## Slide 39: This is the schedule after II Violation Resolved
Seems that HLS is smart enough to build an efficient adder tree

## Slide 40: Loop Partial Unroll
for(int i = 0; i < X; i++)
{
#pragma HLS unroll complete
a[i] = b[i] + c[i];
}
for(int i = 0; i < X; i++)
{
#pragma HLS unroll factor=2
a[i] = b[i] + c[i];
}
X must be known at compile time
Why?
X can be unknown at compile time
Why?
for(int i = 0; i < X; i += 2)
{
a[i] = b[i] + c[i];
if (i+1 >= X) break;
a[i+1] = b[i+1] + c[i+1];
}
HLS can add a condition check
Question: Does this mean partial unroll can replace loop tiling?

## Slide 41: Loop Tiling v.s. Partial Unroll
When to use which?
 | Loop Tiling | Partial Unroll
# of loops | Can tile nested loops (e.g., processing a tensor) | Single loop
Memory | Can optimize memory access pattern (e.g., load a smaller tensor) | Do not optimize memory
Across-iteration accumulation | Can address accumulations (as in previous example) | Cannot address accumulations
Together with pipeline | Yes | Pipeline will override partial unroll and change to complete unroll

## Slide 42: More Loop Optimizations
Initial Interval (II) Violation
Pipeline and Unroll over Functions
Loop-carried Dependency
  Loop reorder
  Remove false dependency
Loop Tiling and Partial Unroll
Loop Fusion
  Parallel loops fused into single loop
  Wrap loops into functions

## Slide 43: Loop Fusion
When we have multiple loops, and they are independent:
for(int i = 0; i < I1; i++)
Do_Homework(i);
for(int j = 0; j < I2; j++)
Watch_A_Movie(j);
for(int i = 0; i < max(I1, I2); i++)
if(i < I1) Do_Homework(i);
if(i < I2) Watch_A_Movie(i);
// definition
Do_Homework_Wrapper() { first_for_loop}
Watch_A_Movie_Wrapper() { second_for_loop}
// function call
Do_Homework_Wrapper();
Watch_A_Movie_Wrapper();
Merge into one
Wrap them up

## Slide 44: Summary – Loop Optimizations
Initial Interval (II) Violation
  Can be caused by unpartitioned array, memory port limitation, repeated accumulation, true/false dependencies, etc.
  Loop transform (change orders), create local buffers, etc.
Pipeline and Unroll over Functions
Loop-carried Dependency
  Loop reorder
  Remove false dependency
Loop Tiling: controlled parallelism – not too large!
Loop Fusion
  Parallel loops fused into single loop or wrap loops into functions
There are many more tricks/pitfalls – I hope I can tell you all of them but impossible to enumerate
Hopefully, you can learn how to fix them on your own (Xilinx manual, etc.)