## Slide 1: Data Type and Quantization
Cong (Callie) Hao
callie.hao@ece.gatech.edu
Assistant Professor
ECE, Georgia Institute of Technology
  Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/

## Slide 2: Hardware Design with HLS
Where does performance gain come from?
Specialization
Parallelization
Data-type
  Arbitrary fixed-point precision, customized floating-point precision
Memory and data movement
  Customized data storage in banks
  Customized data loading and feeding
Computation
  How do you schedule the computations?
    Order, granularity, etc.
Operation level parallelism
  Multiple operations or instructions executed simultaneously
  Mostly about loop manipulation and data partitioning
Task level parallelism (TLP)
  Dataflow and streaming
  Overlapped compute and data movement

## Slide 3: Why Datatype Matters
Data Type = Architecture Decision
Data type determines:
  DSP usage
  BRAM / URAM capacity
  Memory bandwidth
  Pipeline depth & II
On FPGA:
  Saving 1 bit can save DSPs, buffers, and routing
Many 10×–100× speedups come from:
  Data-type specialization, not algorithm changes

## Slide 4: Outline
Floating-point and fixed-point representations
Data quantization in Machine Learning

## Slide 5: Binary Number Representation
Unsigned number
MSB has weight 2n-1
Signed number
MSB has weight -2n-1
decimal point

## Slide 6: IEEE 754 Floating Point Standard
Mantissa (23-bit)
Exponent (8-bit)
Value
decimal point

## Slide 7: Using Existing Data Types in Hardware
C/C++ only provides a limited set of native integer types
  Integers: char (8b), short (16b), int (32b), long (?), long long (64b)
  Floating: single (32b), double (64b), half (16b)
    Single (FP32): E8M23
    Double (FP64): E10M53
    Half (FP16): E5M10
    (recent) BF16: E8M7
Floating point operations are expensive: alignment and scaling
What if you need only 2 bits, or you want 40 bits?

## Slide 8: Arbitrary Data Precision using FPGA
Arbitrary precision integers:
  Signed: ap_int<W>
  Unsigned: ap_uint<W>
  W is the user-specified bitwidth
Arbitrary precision fixed-point representation: for decimal numbers
  Templatized class ap_fixed<W, I, Q, O>
  W: total binary bits
  I: number of integer bits (including sign bit)
  Q: quantization mode
  O: overflow mode
#include “ap_int.h”
…
ap_int<9> x; // 9-bit
ap_uint<17> y; // 17-bit unsigned
ap_uint<512> z; // 512-bit unsigned

## Slide 9: Example: Fixed-Point Modeling
ap_ufixed<11, 8, AP_TRN, AP_WRAP> x;
b7 | b6 | b5 | … | b1 | b0 | … | b-3
11 is the total number of bits in the type
8 bits is the integer bitwidth
AP_TRN defines truncation behavior for quantization
AP_WRAP defines wrapping behavior for overflow

## Slide 10: Fixed-Point Representation
Fix the decimal point → Fixed-point numbers
23 | 22 | 21 | 20 | 2-1 | 2-2 | unsigned
1 | 0 | 1 | 1 | 0 | 1 | 11.25
23 | 22 | 21 | 20 | 2-1 | 2-2 | 2’C
1 | 0 | 1 | 1 | 0 | 1 | ?
decimal point

## Slide 11: Fixed-Point Representation
Fix the decimal point → Fixed-point numbers
23 | 22 | 21 | 20 | 2-1 | 2-2 | unsigned
1 | 0 | 1 | 1 | 0 | 1 | 11.25
23 | 22 | 21 | 20 | 2-1 | 2-2 | 2’C
1 | 0 | 1 | 1 | 0 | 1 | -4.75
decimal point
(-8 + 3.25)

## Slide 12: Floating-Point vs Fixed-Point on FPGA
Operation | Floating-point | Fixed-point
Add | align + normalize | integer add
Mul | mantissa × mantissa; exponent + exponent | integer mul
Latency | Multi-cycle | 1–2 cycle
DSP usage | Very high | Very friendly
Pipeline | Challenging | Very friendly
Floating-point requires:
  Exponent alignment
  Mantissa normalization
  Extra control logic
Floating-point on FPGA:
  High DSP usage
  Multi-cycle latency
  Harder to pipeline
Fixed-point on FPGA:
  Integer arithmetic
  Simple pipelines
  Predictable latency

## Slide 13: Fixed-Point Overflow and Underflow
Overflow: happens at MSB
  When a number is larger than the largest that can be represented
Drop MSB
Underflow: happens at LSB
  When a number is smaller than the smallest that can be represented

## Slide 14: Handling Overflow
Wrapping is one common (& efficient) way of handling overflow: drop the MSBs of the original number
  But… may result in a totally wrong number
Saturation: Overflow "saturates" to the maximum or minimum representable value

## Slide 15: Overflow Modes in HLS
*AP_SAT Requires extra complex logic
default

## Slide 16: Handling Overflow Manually
AP_SAT requires extra complex logic (uses a lot of resource)
Manually handle overflow examples:
  Explicit clipping
  Use larger bitwidth, e.g., larger W
  Rescaling beforehand – do a comprehensive data range analysis
  Ignore it if only happen rarely – in error-resilient algorithms, e.g., machine learning
float a = 176.18793;
ap_fixed<W, I> var = if (a > xxx ) ? clip_value : zzz;

## Slide 17: Handling Underflow – Rounding
Rounding: when a number cannot be represented precisely in a given number of fractional bits (also called quantization)
Rounding down (round to negative infinity): drop the extra fractional bits (LSBs)
  Result in numbers that are more negative

## Slide 18: Handling Underflow – Rounding
Rounding to nearest even: always picks the nearest representable number
  Minimizes rounding errors
  Error tends to cancel out when computing sums – unbiased rounding
Goes larger
Goes smaller

## Slide 19: Quantization Modes in HLS
default
(to nearest)

## Slide 20: Pros and Cons of Fixed Point
Pros
  Low memory, low resource (DSP, peripheral logic), low latency
Cons
  Uncertain accuracy
Vitis HLS can also synthesize floating point
  Requires significant amount of computation → a large amount of resource usage and many cycles of latency
  Floating point numbers should be avoided unless absolutely necessary

## Slide 21: Pitfalls of using Fixed-Point
Representation is fine, but when comes to computation:
  Intermediate results, especially accumulations, matter a lot
  Usually use a larger precision for accumulation
  Maybe other cases
Accumulation error grows with:
  Loop trip count
  Reduction (accumulation) depth
  Sum overflows
Example:
  8-bit × 8-bit → 16-bit product
  Accumulating 256 terms → needs +8 bits
for (int i = 0; i < N; i++) {
for (int j = 0; j < N; j++) {
ap_fixed_higher_precision sum = 0;
for (int k = 0; k < N; k++) {
sum += A[i][k] * B[k][j];
}
}
C[i][j] = sum;
}

## Slide 22: Outline
Floating-point and fixed-point representations
Data quantization in Machine Learning

## Slide 23: Quantization for Machine Learning
Why do we care?
  Faster, smaller, easier!
Why does it work?
Quantization Methods
  Fixed-point
  Integer
Reference: https://sahnimanas.github.io/post/quantization-in-tflite/

## Slide 24: Why Does Quantization Work for ML?
DNNs are known to be robust to noise and small perturbations once trained
  80% chance to be a dog? 75% chance to be a dog? Still a dog!
Cat: 0.1
Dog: 0.7
Bird: 0.1
Parrot: 0.1

## Slide 25: Why Does Quantization Work for ML?
DNNs are known to be robust to noise and small perturbations once trained
  80% chance to be a cat? 75% chance to be a cat? Still a cat!
Weights and activations often tend to lie in a small range
  Can be estimated beforehand

## Slide 26: Quantization Method 1 – Fixed Point
Using fixed-point instead of floating point: most widely used in HLS
Drawback: doesn’t work well for low bit-width, e.g., < 8-bit
  The range of the represented number is strictly limited by W and I
sign | b2 | b1 | b0
[-4, 3.5]
step: 0.5
#include “ap_fixed.h”
Typedef ap_fixed<9, 3> my_fixed_type;
my_fixed_type weights[dim1][dim2];
my_fixed_type bias[dim1];
…
weights[0][0] = (my_fixed_type) weights_float[0][0];
…
sign | b2 | b1 | b0
[-2, 1.75]
step: 0.25

## Slide 27: Quantization Method 2 – Integer
With a scaling and a bias (shift), can represent a much larger range
https://intellabs.github.io/distiller/algo_quantization.html
8-bit
: original floating-point value
q : quantized integer
scale and bias: can be floating or fixed point

## Slide 28: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7

## Slide 29: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Scaling factor

## Slide 30: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-4.47 | -2.03 | -0.11 | 0.00 | 0.32 | 0.44 | 1.16 | 1.34 | 2.22 | 2.53
Next is to shift

## Slide 31: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-4.47 | -2.03 | -0.11 | 0.00 | 0.32 | 0.44 | 1.16 | 1.34 | 2.22 | 2.53
(is this the best choice?)

## Slide 32: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-4.47 | -2.03 | -0.11 | 0.00 | 0.32 | 0.44 | 1.16 | 1.34 | 2.22 | 2.53
0.00 | 2.44 | 4.36 | 4.47 | 4.79 | 4.91 | 5.63 | 5.81 | 6.69 | 7.00

## Slide 33: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-4.47 | -2.03 | -0.11 | 0.00 | 0.32 | 0.44 | 1.16 | 1.34 | 2.22 | 2.53
0.00 | 2.44 | 4.36 | 4.47 | 4.79 | 4.91 | 5.63 | 5.81 | 6.69 | 7.00

## Slide 34: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-4.47 | -2.03 | -0.11 | 0.00 | 0.32 | 0.44 | 1.16 | 1.34 | 2.22 | 2.53
0.00 | 2.44 | 4.36 | 4.47 | 4.79 | 4.91 | 5.63 | 5.81 | 6.69 | 7.00
Zeros are very common in ML but are tampered

## Slide 35: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-4.47 | -2.03 | -0.11 | 0.00 | 0.32 | 0.44 | 1.16 | 1.34 | 2.22 | 2.53
0.53 | 2.97 | 4.89 | 5.00 | 5.32 | 5.44 | 6.16 | 6.34 | 7.22 | 7.53
A better approach: align the zero!

## Slide 36: Quantization Method 2 – Integer (Example)
-257.8 | -117.2 | -6.3 | 0 | 18.4 | 25.3 | 66.9 | 77.3 | 128.1 | 145.6
3-bit: 23 = 8
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-4.47 | -2.03 | -0.11 | 0.00 | 0.32 | 0.44 | 1.16 | 1.34 | 2.22 | 2.53
0.53 | 2.97 | 4.89 | 5.00 | 5.32 | 5.44 | 6.16 | 6.34 | 7.22 | 7.53
A better approach: align the zero!
Many researches are trying to find the optimal scaling factor and bias…

## Slide 37: Fixed-Point vs Integer Quantization
Key Difference: Coupled vs Decoupled Range
Fixed-point:
  Range determined by I
  Precision determined by W − I
  Strongly coupled
Integer quantization:
  Range controlled by scale + bias
  Precision controlled by integer bit-width
  Decoupled design
Integer quantization enables ultra-low-bit inference

## Slide 38: When to Use What (Decision Guide)
Choosing the Right Numeric Representation
Floating-point:
  High dynamic range
  Control-heavy logic
Fixed-point:
  Medium precision
  Known ranges
Integer quantization:
  ML inference
  ≤8-bit
  High efficiency
Precision choice = performance choice

## Slide 39: Summary
Floating point representation
Fixed point representation
  Overflow, underflow, rounding
Data quantization in Machine Learning
  Two approaches