## Slide 1: Memory and Data Movement
Cong (Callie) Hao
callie.hao@ece.gatech.edu
Assistant Professor
ECE, Georgia Institute of Technology
  Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/

## Slide 2: Hardware Design with HLS
Where does performance gain come from?
Specialization
Parallelization
Data-type
  Arbitrary fixed-point precision, customized floating-point precision
Memory and data movement
  Customized data storage in banks
  Customized data loading and feeding
Computation
  How do you schedule the computations?
    Order, granularity, etc.
Operation level parallelism
  Multiple operations or instructions executed simultaneously
  Mostly about loop manipulation and data partitioning
Task level parallelism (TLP)
  Dataflow and streaming
  Overlapped compute and data movement

## Slide 3: Memory Performance: 3 knobs
Bandwidth: how many bits per cycle you could move
  burst, wide bus, vector types
Reuse: how many times you use data after paying to fetch it
  local buffers, partitioning
Overlap: whether compute waits for memory
  double buffering, streaming, dataflow

## Slide 4: Outline
Burst mode
Wide bus transaction
Double Buffer
Streaming
C/RTL Co-simulation

## Slide 5: DRAM Data Access
Large overhead (setup time) for each data access from/to DRAM
  Co-sim shows 2 cycles (older version shows 16 cycles); on-FPGA can be even larger
Y. Y. Chew et al.: In-Depth Review and Comparative Analysis of DRAM-Based PUFs

## Slide 6: Burst Mode
Setup once, transfer multiple data chunks
  The larger burst size, the better

## Slide 7: Burst Mode for Continuous Memory Access
void test( FIX_TYPE A[100][100], ...) {
#pragma HLS interface m_axi port=A offset=slave bundle=mem
FIX_TYPE A_local[100][100];
for(int i = 0; i < 100; i++) {
for(int j = 0; j < 100; j++) {
A_local[i][j] = A[i][j];
}
}
...
}
How do you like this design?
What’s its best performance?
Assume it’s 32-bit
32-bit per cycle

## Slide 8: Burst Mode for Continuous Memory Access
void test( FIX_TYPE A[100][100], ...) {
#pragma HLS interface m_axi port=A offset=slave bundle=mem
FIX_TYPE A_local[100][100];
for(int i = 0; i < 100; i++) {
for(int j = 0; j < 100; j++) {
A_local[i][j] = A[i][j];
}
}
...
}
Multiple burst reads of length 10000 and bit width 32 in loop xxx has been inferred on port 'mem'
Enable burst mode whenever possible by using continuous memory access

## Slide 9: Bad Practice
for(int i = 0; i < 100; i++) {
for(int j = 0; j < 100; j+=2) {
A_local[i][j] = A[i][j];
}
}
for(int j = 0; j < 100; j++) {
for(int i = 0; i < 100; i++) {
A_local[i][j] = A[i][j];
}
}
Do not burst because memory is not continuous
> 12000 cycles (expected 5000)
> 20000 cycles (expected 10000)

## Slide 10: Wider Bus Transaction
void test( FIX_TYPE A[100][100], ...) {
#pragma HLS interface m_axi port=A offset=slave bundle=mem
FIX_TYPE A_local[100][100];
for(int i = 0; i < 100; i++) {
for(int j = 0; j < 100; j++) {
A_local[i][j] = A[i][j];
}
}
...
}
Assume it’s 32-bit
32-bit per cycle
Is this good enough?
AXI bus is 512 bit wide – 15/16 bandwidth is wasted!

## Slide 11: Outline
Burst mode
Wide bus transaction
Double Buffer
Streaming
C/RTL Co-simulation

## Slide 12: Wider Bus Transaction
32b | 32b | 32b | 32b | 32b | 32b | 32b | 32b | 32b | 32b
32b
...
32b
...
32b
...
32b
...
32b
...
32b
...
32b
...
32b
...
32b
...
32b
...
320-bit customized datatype
Partitioned local arrays

## Slide 13: Wider Bus Transaction
typedef ap_uint<320> MEM_TYPE;
void test( MEM_TYPE A[100*10], ...) {
#pragma HLS interface m_axi port=A offset=slave bundle=mem
FIX_TYPE A_local[100*100];
#pragma HLS array_partition variable=A_local cyclic factor=10
for(int i = 0; i < 100*10; i++) {
#pragma HLS pipeline
MEM_TYPE data = A[i];
for(int ii = 0; ii < 10; ii++) {
A_local[i*10 + ii] = data.range(0 + (ii*32), 31 + (ii*32));
}
}}
...
}
Create a customized wide data type – 320 bit
[INFO] Multiple burst reads of length 1000 and bit width 512
Reorganize into 1D array
Read 320 bit at each cycle

## Slide 14: Use HLS Vector
hls::vector<T, N>: to model and synthesize single instruction multiple data (SIMD) type operations
  T: The type of elements in the vector; can be a user-defined type
  N: The number of elements that the vector holds
  The best performance is achieved when both the bit-width of T and N are integer powers of 2
HLS will reconfigure the BRAM port width to support a vector
typedef hls::vector<int, 8> int8Vec;
int8Vec intVectorA, intVectorB;
void processVecStream(hls::stream<int8Vec> &inVecStream1,
hls::stream<int8Vec> &inVecStream2,
hls::stream<int8Vec> &outVecStream)
{
for(int i=0;i<32;i++) {
#pragma HLS pipeline II=1
t_int8Vec aVec = inVecStream1.read();
t_int8Vec bVec = inVecStream2.read();
t_int8Vec cVec = aVec * bVec;
outVecStream.write(cVec);
}
}
int | int | int | int | int | int | int | int
aVec
int | int | int | int | int | int | int | int
bVec

## Slide 15: Outline
Burst mode
Wide bus transaction
Double Buffer
Streaming
C/RTL Co-simulation

## Slide 16: Single Buffer Limitation
Read-Execute-Write create dependency
Execution
PE
Input Buffer
(BRAM)
Load
PE
Store
PE
DRAM
DRAM
Output Buffer
(BRAM)
*PE: processing element
buf1
buf2

## Slide 17: Single Buffer Limitation
Read-Execute-Write create dependency
Load
Cannot execute on buf1 if the load function is unfinished
buf1
buf2

## Slide 18: Single Buffer Limitation
Read-Execute-Write create dependency
Execute
buf1
buf2
Cannot write buf2 to DRAM if the execution function is unfinished

## Slide 19: Single Buffer Limitation
Read-Execute-Write create dependency
Store
buf1
buf2

## Slide 20: Single Buffer Limitation: Read-After-Write
Single buffer forces serialization
The compiler must assume that buffer is a random-access array; therefore, any element may be:
  read at any time
  overwritten at any time
Consequence:
  Compute cannot start until all reads finish
  Store cannot start until all writes finish
  Operations are forced to run sequentially

## Slide 21: Overlap Read and Write (Pre-fetching)
for(int i = 0; i < N; i++) {
load(buf_A, i);
execute(buf_A, buf_B);
store(buf_B, i);
}
Load
Execute
Store
load(buf_A, i);
for(int i = 0; i < N; i++) {
execute(buf_A, buf_B);
store(buf_B, i);
if(i < N-1) load(buf_A, i+1);
}
Load
Execute
Store
Load
Load latency is hidden by overlapping with Store
But what about Store latency?

## Slide 22: Double Buffer (Ping-Pong Buffer)
Load
Execute
Store
Load
Execute
Store
Now Load and Execute can work in parallel even though they have dependencies

## Slide 23: Double Buffer (Ping-Pong Buffer)
load(buf_A_Ping, i);
for(int i = 0; i < N; i++) {
if( i % 2 == 0 ) {
if( i < N-1 ) load(buf_A_Pong, i+1);
execute(buf_A_Ping, buf_B);
store(buf_B, i);
}
else if (i % 2 == 1) {
if( i < N-1 ) load(buf_A_Ping, i+1);
execute(buf_A_Pong, buf_B);
store(buf_B, i);
}
}
Load and Execute can work in parallel by using two different buffers
Load and Execute can work in parallel by using two different buffers

## Slide 24: Double Buffer (Ping-Pong Buffer)
for(int i = 0; i < N; i++) {
if( i % 2 == 0 ) {
execute(buf_A_Ping, buf_B_Ping);
if( i > 0 ) store(buf_B_Pong, i-1);
if( i < N-1 ) load(buf_A_Pong, i+1);
}
else if (i % 2 == 1) {
execute(buf_A_Pong, buf_B_Pong);
if( i > 0 ) store(buf_B_Ping, i-1);
if( i < N-1 ) load(buf_A_Ping, i+1);
}
}
read(buf_A_Ping, i);
if( xxx ) store(buf_B_Ping, i);
else
store(buf_B_Pong; i);

## Slide 25: Ping-Pong Buffer Pros and Cons
Pros
  Overlapped execution – shorter latency
Cons
  Memory overhead (2x)
  Programmer’s effort

## Slide 26: Hidden Assumption Behind Ping-Pong
Ping-pong still assumes array-style memory semantics
  Buffers are treated as random-access arrays
Compiler assumes:
  Any element may be read at any time
  Any element may be overwritten at any time
Therefore:
  Full buffer must be written before it is safe to read
  Full buffer must be read before it is safe to overwrite
Consequence:
  Dependencies are conservative
  Scheduling is rigid
  Programmer effort increases quickly with more stages

## Slide 27: Do We Really Need Random Access?
Many designs don’t need full arrays at all; data is often
  produced in order
  consumed in order
  never revisited
This is not memory — this is a stream
If access order is fixed:
  compiler does not need to wait for “all writes”
If order is fixed, correctness can be enforced by ordering, not completion.

## Slide 28: Break the Dependency using FIFOs
Is there a better way?  Why is the dependency enforced?
Key assumption is the write and read can be random order
  To ensure correctness, function_2 cannot touch array_A unless all writes are done
What if the design only need a fixed order?
function_1
function_2
function_3
array_A
array_B

## Slide 29: Producer-Consumer Paradigm

## Slide 30: Data Streaming for Producer-Consumer
Enabled by FIFO (first-in first-out) buffers
  The consumer process can start accessing the data inside the FIFO buffer as soon as the producer inserts the data into the buffer
  If the buffer is full/empty, automatically stalls
function_1
function_2
function_3
array_A
array_B
FIFO
FIFO
function_1
function_2
function_3

## Slide 31: Data Streaming for Producer-Consumer
Enabled by FIFO (first-in first-out) buffers
  The consumer process can start accessing the data inside the FIFO buffer as soon as the producer inserts the data into the buffer
  If the buffer is full/empty, automatically stalls
FIFO
FIFO
function_1
function_2
function_3
To be more general, this is called Task Level Parallelism (TLP)

## Slide 32: Outline
Burst mode
Wide bus transaction
Double Buffer
Streaming
C/RTL Co-simulation

## Slide 33: Resource Utilization
Resource utilization (DSP, LUT, BRAM) and latency value
  These are only estimation by Vitis HLS – not reliable!
    I’m surprised by how inaccurate the estimation could be… (they used to be fine at least for DSPs…)
What to do?!
  C/RTL co-simulation or LightningSim – to get actual cycle counts
  Apply implementation – really map those generated RTL onto FPGA

## Slide 34: Vitis HLS Flow – Recap
C Simulation (C-sim)
C Synthesis (C-syn)
// Host code
// A.k.a., testbench
// HLS design
C/RTL Co-simulation (Co-sim)
RTL Synthesis
Placement and Routing
bitstream
program
FPGA
RTL (Verilog)

## Slide 35: Synthesis v.s. Implementation
This is what you get from Synthesis report
Performance and Resource Estimation

## Slide 36: Synthesis v.s. Implementation
Run Implementation in GUI

## Slide 37: Synthesis v.s. Implementation
Implementation
Synthesis

## Slide 38: Summary
Widening the memory port – fully utilize DRAM bandwidth
Double buffer to hide the data loading latency
More advanced (challenging) technique: streaming and dataflow
  More generally, Task Level Parallelism (TLP)