## Slide 1: Task Level Parallelism (TLP) Dataflow and hls::task
Cong (Callie) Hao
callie.hao@ece.gatech.edu
Assistant Professor
ECE, Georgia Institute of Technology
  Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/

## Slide 2: Hardware Design with HLS
Where does performance gain come from?
Specialization
Parallelization
Data-type
  Arbitrary fixed-point precision, customized floating-point precision
Memory and data movement
  Customized data storage in banks
  Customized data loading and feeding
Computation
  How do you schedule the computations?
    Order, granularity, etc.
Operation level parallelism
  Multiple operations or instructions executed simultaneously
  Mostly about loop manipulation and data partitioning
Task level parallelism (TLP)
  Dataflow and streaming
  Overlapped compute and data movement

## Slide 3: Materials
Resources:
  Vitis Example: https://github.com/Xilinx/Vitis-HLS-Introductory-Examples/tree/master/Task_level_Parallelism/Data_driven/simple_data_driven
  Vitis Manual:
    HLS task: https://docs.amd.com/r/2024.1-English/ug1399-vitis-hls/HLS-Task-Library
    HLS dataflow: https://docs.amd.com/r/2024.1-English/ug1399-vitis-hls/pragma-HLS-dataflow
  Article: https://www.xilinx.com/developer/articles/task-level-parallelism-and-pipelining-in-hls.html

## Slide 4: Consider this example
void subM(int in1[128], int in2[128], int out[128]) { int tmp1[128], tmp2[128], tmp3[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
void topM() { for(int i = 0; i < 4; i++)
// calling subM with different arrays
subM(...);
}
Sub-module
Top-module

## Slide 5: Zero Optimization
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out

## Slide 6: What We Want
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
What to do?
Task level parallelism

## Slide 7: First Optimization – Dataflow within SubM
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
void subM(int in1[128], int in2[128], int out[128]) {
#pragma HLS dataflow int tmp1[128], tmp2[128], tmp3[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}

## Slide 8: First Optimization – Dataflow within SubM
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
By default, HLS dataflow uses ping-pong buffers
So that double_increase and increase can avoid memory conflict
Same for other buffers

## Slide 9: First Optimization – Dataflow within SubM
double_increase
increase
add
tmp1B
in1
in2
tmp2A
tmp3A
out
tmp2B
tmp1A
tmp3B
Must follow dataflow canonical form

## Slide 10: Second Optimization – Dataflow of TopM
void subM(int in1[128], int in2[128], int out[128]) {
#pragma HLS dataflow int tmp1[128], tmp2[128], tmp3[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
void topM() {
#pragma HLS dataflow for(int i = 0; i < 4; i++)
// calling subM with different arrays
subM(...);
}

## Slide 11: Canonical Form
void dataflow_top(Input0, Input1, Output0, Output1)
{
for (int i = 0; i < N; i++) {
#pragma HLS dataflow
custom_arrays C0, C1, C2;
func1(read_Input0, read_Input1, write_C0, write_C1);
func2(read_C0, read C1, write_C2);
func3(read_C2, write_Output0, write_Output1);
}
}
func1
func1
func1
C0
C1
C2

## Slide 12: Canonical Form
Single Producer, Single Consumer – everything must be streamlined, no bypass
No Feedback between tasks
No Conditional execution of tasks
No Loops with multiple exit conditions
FIFO
FIFO
FIFO

## Slide 13: Canonical Form
Single Producer, Single Consumer – everything must be streamlined, no bypass
No Feedback between tasks
No Conditional execution of tasks
No Loops with multiple exit conditions
FIFO
FIFO
FIFO
Dataflow Region

## Slide 14: Canonical Form
Single Producer, Single Consumer – everything must be streamlined, no bypass
No Feedback between tasks
No Conditional execution of tasks
No Loops with multiple exit conditions
FIFO
FIFO
FIFO
Dataflow Region

## Slide 15: Canonical Form
Single Producer, Single Consumer – everything must be streamlined, no bypass
No Feedback between tasks
No Conditional execution of tasks
No Loops with multiple exit conditions
FIFO
FIFO
FIFO
Dataflow Region

## Slide 16: Dataflow within SubM
double_increase
increase
add
tmp1B
in1
in2
tmp2A
tmp3A
out
tmp2B
tmp1A
tmp3B
Does this follow canonical form?

## Slide 17: Dataflow within SubM
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
Stage 1
Stage 2
Stage 3
Violation: array tmp1 is not consumed but bypassed in the second pipeline stage
nothing

## Slide 18: Dataflow within SubM
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
Stage 1
Stage 2
Lead to performance degradation by reducing pipeline stages and increasing pipeline interval
How to address this problem?

## Slide 19: Third Optimization – Revised Dataflow
void dut(int* in1, int* in2, int* out) {
#pragma HLS dataflow int tmp1[128], tmp2[128];
int tmp3[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
void dut(int* in1, int* in2, int* out) {
#pragma HLS dataflow int tmp1[128], tmp2[128];
int tmp3[128], tmp4[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3, tmp1, tmp4);
add(tmp4, tmp3, out);
}

## Slide 20: Third Optimization – Revised Dataflow
void dut(int* in1, int* in2, int* out) {
#pragma HLS dataflow int tmp1[128], tmp2[128];
int tmp3[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
double_increase
add
tmp1
in1
in2
tmp2
tmp3
out
void dut(int* in1, int* in2, int* out) {
#pragma HLS dataflow int tmp1[128], tmp2[128];
int tmp3[128], tmp4[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3, tmp1, tmp4);
add(tmp4, tmp3, out);
}
increase
tmp4
Drawback??

## Slide 21: Drawbacks
double_increase
add
tmp1
in1
in2
tmp2
tmp3
out
increase
tmp4
All buffers are doubled – a huge resource overhead
Introduce additional buffers and (maybe) dummy computations

## Slide 22: Fourth Optimization – Use FIFOs (streaming)
void subM(int* in1, int* in2, int* out) {
#pragma HLS dataflow int tmp1[128], tmp2[128];
int tmp3[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
void subM(int* in1, int* in2, int* out) {
#pragma HLS dataflow hls::stream<int, 4> tmp1;
hls::stream<int, 4> tmp2, tmp3; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}

## Slide 23: Fourth Optimization – Use FIFOs (streaming)
double_increase
increase
add
tmp1
in1
in2
tmp2
tmp3
out
void subM(int* in1, int* in2, int* out) {
#pragma HLS dataflow hls::stream<int, 4> tmp1;
hls::stream<int, 2> tmp2, tmp3; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
FIFOs:
Fixed ordered read and write
Therefore simultaneous read and write
Now, increase does not need to wait until double_increase finishes!

## Slide 24: Fourth Optimization – Use FIFOs (streaming)
double_increase
increase
add
in1
in2
out
If FIFO is full/empty: automatically stall
Otherwise, keep writing to or reading from
Almost optimal solution
Bonus benefit?
Potential challenges?

## Slide 25: Fourth Optimization – Use FIFOs (streaming)
void subM(int* in1, int* in2, int* out) {
#pragma HLS dataflow int tmp1[128], tmp2[128];
int tmp3[128]; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
void subM(int* in1, int* in2, int* out) {
#pragma HLS dataflow hls::stream<int, 4> tmp1;
hls::stream<int, 4> tmp2, tmp3; double_increase(in1, in2, tmp1, tmp2);
increase(tmp2, tmp3);
add(tmp1, tmp3, out);
}
Very efficient resource usage! No more huge or doubled arrays
Bonus benefit?
FIFO sizing: can easily result in deadlock or stall
Potential challenges?
If change tmp1 size from 4 to 2: latency 517  769
If change tmp1 size from 2 to 1: latency 769  1536

## Slide 26: Where do Deadlocks Come From?
transpose
elementwise_cos
elementwise_add
copy_stream
Simultaneous
Writes
Simultaneous
Reads
Buffer many elements in for a single write
Compute and write out immediately after a read
STALLED
!
STALLED
!
STALLED
!
STALLED
!
Deadlocked Forever

## Slide 27: Another example of deadlock
load_inputs
compute_add
store_result
FIFO1
FIFO2
FIFO3
Input from external memory
Output to external memory
Assume:
FIFO1 and FIFO2 comes from the same external memory port
FIFO1 and FIFO2 will be read in bulk, e.g., 16 elements, to enable burst data transfer
Deadlock when:
FIFO1 and FIFO2 sizes are smaller than 16

## Slide 28: LightningSim + FIFOAdvisor
Incremental stall and deadlock analysis
Suggest optimal FIFO depth
#define FIFO_DEPTH 3
void top(...)
{
#pragma HLS DATAFLOW
hls::stream<int, FIFO_DEPTH> myFIFO;
producer( myFIFO );
...
consumer( myFIFO );
}
Current FIFO depth is 3 but it is deadlocking…
Change to 5? 8? 100?
  Too large: consumes too much resource
  Too small: may still deadlock or stall

## Slide 29: LightningSim + FIFOAdvisor
Incremental stall and deadlock analysis
Suggest optimal FIFO depth
  LightningSim flow:
  no source code change, no RTL re-generation, no co-sim re-run!
HLS
C/C++
RTL Generation
Static Timing Info.
RTL
code
C/RTL cosim
HLS synthesis
Scheduling and Binding
LLVM IR
Bitcode
Front-end
Compilation
LightningSim
Trace generation
Trace analysis
1
2
Vitis HLS flow: change HLS source code, re-run everything…
And do it again and again and again…

## Slide 30: Data Streaming in HLS
Step 1: create FIFOs using hls::stream<type>
  Specify a depth (how large the FIFO is)
Step 2: organize into two functions or loops
  One writing to FIFO, one reading from FIFO
Step 3: apply dataflow pragma

## Slide 31: Data Streaming in HLS – Example
void test( FIX_TYPE* A, FIX_TYPE* sum ) {
#pragma HLS dataflow
hls::stream<FIX_TYPE> buffer;
#pragma HLS STREAM variable=buffer depth=10
READ_A: for(int i = 0; i < 100; i++) {
buffer.write(A[i]);
}
COMPUTE_RES: for(int i = 0; i < 100; i++) {
FIX_TYPE d = buffer.read();
FIX_TYPE res = d * d + i;
sum[i] = res;
}
}

## Slide 32: Data Streaming in HLS – Example
void test( FIX_TYPE* A, FIX_TYPE* sum ) {
#pragma HLS dataflow
hls::stream<FIX_TYPE> buffer;
#pragma HLS STREAM variable=buffer depth=10
READ_A: for(int i = 0; i < 100; i++) {
buffer.write(A[i]);
}
COMPUTE_RES: for(int i = 0; i < 100; i++) {
FIX_TYPE d = buffer.read();
FIX_TYPE res = d * d + i;
sum[i] = res;
}
}

## Slide 33: Data Streaming in HLS – Example
void test( FIX_TYPE* A, FIX_TYPE* sum ) {
#pragma HLS dataflow
hls::stream<FIX_TYPE> buffer;
#pragma HLS STREAM variable=buffer depth=10
READ_A: for(int i = 0; i < 100; i++) {
buffer.write(A[i]);
}
COMPUTE_RES: for(int i = 0; i < 100; i++) {
FIX_TYPE d = buffer.read();
FIX_TYPE res = d * d + i;
sum[i] = res;
}
}

## Slide 34: HLS Task: An Alternative Way
The original DATAFLOW model lets you write sequential functions, and then requires the AMD Vitis HLS tool to identify dataflow processes (tasks) and make them parallel
Alternatively, the use of hls::task requires you to explicitly instantiate tasks and channels, managing parallelization yourself in your algorithm design.
The purpose of hls::task is to define a programming model that supports parallel tasks using only streaming data channels
Long story short: hls::task is more flexible and you have better control, but needs more expertise

## Slide 35: HLS Task Example
void odds_and_evens(hls::stream<int>& in,
hls::stream<int>& out1,
hls::stream<int>& out2)
{
hls_thread_local hls::stream<int, N / 2> s1; // channel connecting t1 and t2
hls_thread_local hls::stream<int, N / 2> s2; // channel connecting t1 and t3
// t1 infinitely runs func1, with input in and outputs s1 and s2
hls_thread_local hls::task t1(splitter, in, s1, s2);
// t2 infinitely runs func2, with input s1 and output out1
hls_thread_local hls::task t2(odds, s1, out1);
// t3 infinitely runs func3, with input s2 and output out2
hls_thread_local hls::task t3(evens, s2, out2);
}
splitter
odds
evens
in
out1
out2
s1
s2

## Slide 36: Summary
Achieving task level parallelism can greatly improve hardware performance (latency, throughput)
Using streaming (FIFO) and dataflow reduces resource utilization (compared with double buffer)
LightningSim helps you very quickly simulate the impact of FIFO depths!